## Slide 1
INDION AKD WP
HIGH PURITY WATER SYSTEM FOR
ARTIFICIAL KIDNEY DIALYSIS

## Slide 2
INTRODUCTION
Artificial way to remove waste and extra fluids from the body
Process of selective diffusion of solutes through membrane
High purity water mixed with electrolytes and salts, such as bicarbonate and sodium to form Dialysate
Heart of Haemodialysis WATER
Patients exposed to large amount of water during dialysis

## Slide 3
    WHY PURIFICATION OF WATER IS REQUIRED ?
Impurities | Allowable Limit (mg/l) | Causes
Aluminum | 0.01 | Dialysis Dementia
Chloramines | 0.1 | Acute Hemolytic Anemia
Fluoride | 0.2 | Toxicity, Bone Diseases
Lead | 0.005 | Gastro Intestinal Pain, Muscle Weakness
Sulphate | 100 | Nausea, Metabolic Acidosis
Calcium | 2 | Hypertension, Nausea, Vomiting
Magnesium | 4 | Muscle Weakness
Nitrate | 2 | Methemoglobinemia
Bacteria | < 100 CFU/ml | Nausea, Vomiting, Bloodstream Infection, Death
Endotoxin | < 0.25 EU/ml | Pyrogenic reaction, Death
Source of Data : Guideline on water treatment systems, dialysis water and dialysis fluid quality for haemodialysis and related therapies prepared on behalf of The Renal Association and The Association of Renal Technologists

## Slide 4
Treated Water Quality
As per AAMI 13959:2014
Microbiological Level | Previous standard | New Standard | Previous Action Level | New Action Level
Colony Forming Units | < 200 CFU/ml | < 100 CFU/ml | = 50 CFU/ml | = 50 CFU/ml
Endotoxin Units | < 2 EU/ml | < 0.25 EU/ml | = 1 EU/ml | = 0.125 EU/ml

## Slide 5
Dialysate

## Slide 6
Assurance of Treated Water Quality

## Slide 7
Scientifically designed system
All pipings are of electro polished stainless steel
Sanitary design of all equipments & components
Hot water sanitisable RO and UF Membranes
UV system post Ultra filtration
PLC controlled system with safety interlocks
Touch screen display
Available both fully auto and semi auto mode with wide range of capacities
Dead lag free system
No risk of bio film formation
Right quality of water as per AAMI standards
Compact and Portable system
Multi stage protection from Bacteria and Endo toxins
Chemical free sanitization
Features
Advantages
AKD- Water Treatment Plant

## Slide 8
AKD- Water Treatment Plant
High rejection of TOC, pyrogens, Bacteria and Endotoxin
Easy system operation
Minimum footprint and easy access for maintenance
Safety in dialysis operation
Benefits

## Slide 9
PROCESS FLOW
Sand Filter
Raw Water Storage Tank
Activated
Carbon Filter
Softener
Micron Cartridge Filter
UV
HSUF
HSRO
PREFILTERATION
Treated Water Storage Tank
To Dialysis Units

## Slide 10
NORMAL RO Vs AKD WP
Description | Normal RO Plant | AKD Water Treatment Plant
Design | Ordinary design | Scientifically designed with no dead lags
Chances of Bio Film Formation | High | Low
MOC of functional components | PVC/MS/PEX/PVDF | Electro polished stainless steel with Ra value < 0.8 µm
RO Membrane | Commercial Grade | Hot Water Sanitisable RO
UF Membrane/ Hollow Cartridge Filter | Not Available | Hot Water Sanitisable/ Auto Clave Sanitisable
Type of Cleaning | Chemical Cleaning | Hot water sanitization and if require chemical cleaning

## Slide 11
AKD- Water Treatment Plant
Scientifically designed system
Suites well for Hygiene Applications
Electro polished Stainless steel with Ra value < 0.8µM
Zero Bio fouling
No PEX/PVDF or Flexible Plastics are used
AKD WP with 400 LPH Capacity

## Slide 12
Hot Water Sanitisable RO membranes
High capability to withstand Hot water sanitization
Full Fit configuration with minimum stagnant area
Comply with FDA standards
Hot Water Sanitisable Ultra filtration
High Water Productivity with large membrane area
High Thermo Durability
Very Low Effluent
Excellent Chemical Resistance
Produces Pyrogens free water
AKD- Water Treatment Plant

## Slide 13
AKD- Water Treatment Plant
Endotoxin removable Hollow fiber Cartridge Filtration (For semi auto systems)
Excellent removal of Bacteria and Endotoxin
High Water Productivity
Higher Filter Life
Sanitary Fittings
Stainless steel Tri clover clamps and ends with High precision machining and Surface polishing
Easy to install and remove for maintenance

## Slide 14
AKD- Water Treatment Plant
Micron Cartridge Filter
Cartridges for Pre filtration provides valuable protection for RO membrane.
High dirt loading capacities, with long service
High Chemical compatibility
High Temperature Sustainable, Food Grade Gaskets for avoiding leakage
Sample points at every stage to ensure quality
Online Conductivity, pH and ORP meters for monitoring quality of water

## Slide 15
AKD- Water Treatment Plant
USER INTERFACE
User friendly 7” touch screen display to control the components

## Slide 16
AKD- WP Vs Competitors
AKD WP - 1500 LPH
Competitor RO for dialysis

## Slide 17
AKD WP - 1500 LPH
Competitor RO for Dialysis
AKD- WP Vs Competitors

## Slide 18
AKD WP - 400 LPH
Competitor RO for Dialysis
AKD- WP Vs Competitors

## Slide 19
FEED WATER CONDITIONS
a. | pH range, Short Term Cleaning | 1-12
b. | Residual Chlorine | Nil
c. | Turbidity | <1 NTU
d. | Suspended solids | Nil
e. | SDI | < 4
f. | Temperature | < 40°C
g. | Organics and Bacteria | Nil
h. | Heavy Metals | < 0.1 ppm
i. | TDS | Potable Water
Sl. No. | Parameters | Inlet water quality

## Slide 20
TECHNICAL SPECIFICATIONS
AKD Basic - Semi Automatic System
Model | AKD-100 | AKD-400 | AKD-1000 | AKD-1500
Type | BASIC Semi Auto | BASIC Semi Auto | BASIC Semi Auto | BASIC Semi Auto
Average product flow(LPH) | 100 | 400 | 1000 | 1500
Average Recovery(%) | 30 | 30-85 | 30-85 | 30-85
Maximum Permissible TDS feed (PPM) | 1500 | 1500 | 1500 | 1500
Average TDS Removable (%) | Between 90-95 | Between 90-95 | Between 90-95 | Between 90-95
Minimum feed pressure required at pump inlet (kg/cm²) | Not less than 1.0 | Not less than 1.0 | Not less than 1.0 | Not less than 1.0
Cartridge Housing | SS316 | SS316 | SS316 | SS316
Cartridge MOC | PP | PP | PP | PP
RO SYSTEM |  |  |  | 
Membrane | 4"-HSRO | 4"-HSRO | 4"-HSRO | 4"-HSRO
Pressure Tube | SS316L | SS316L | SS316L | SS316L
Skid | SS304 | SS304 | SS304 | SS304
Hollow Fibre Cartridge System |  |  |  | 
Cartridge | 0.05 Micron 10” | 0.05 Micron 10” | 0.05 Micron 10” | 0.05 Micron 10”
MOC | SS 316 | SS 316 | SS 316 | SS 316

## Slide 21
HIGH PRESSURE PUMP |  |  |  | 
MOC | SS316 | SS316 | SS316 | SS316
Quantity | 1No | 1No | 1No | 1No
MULTI PURPOSE TANK | SS 316 | SS 316 | SS 316 | SS 316
Skid | SS 304 | SS 304 | SS 304 | SS 304
UV System (Optional) |  |  |  | 
PLC | PLC with 4.3” HMI Display |  |  | 
AKD Basic - Semi Automatic System
TECHNICAL SPECIFICATIONS

## Slide 22
AKD Advanced - Fully Automatic System
Model1 | AKD-100 | AKD-400 | AKD-1000 | AKD-1500
Type | ADV Fully Auto | ADV Fully Auto | ADV Fully Auto | ADV Fully Auto
Average product flow(LPH) | 100 | 400 | 1000 | 1500
Average Recovery(%) | 30 | 30 | 35 | 55
Maximum Permissible TDS feed (PPM) | 1500 | 1500 | 1500 | 1500
Average TDS Removable (%) | Between 90-95 | Between 90-95 | Between 90-95 | Between 90-95
Minimum feed pressure required at pump inlet (kg/cm²) | Not less than 1.0 | Not less than 1.0 | Not less than 1.0 | Not less than 1.0
Cartridge Housing | SS316 | SS316 | SS316 | SS316
Cartridge | PP | PP | PP | PP
RO SYSTEM |  |  |  | 
Membrane | 4"-HSRO | 4"-HSRO | 4"-HSRO | 4"-HSRO
Pressure Tube | SS316L | SS316L | SS316L | SS316L
Skid | SS304 | SS304 | SS304 | SS304
UF SYSTEM |  |  |  | 
Membrane Type | 6000 MWCO | 6000 MWCO | 6000 MWCO | 6000 MWCO
TECHNICAL SPECIFICATIONS

## Slide 23
UV SYSTEM |  |  |  | 
MOC | SS316 | SS316 | SS316 | SS316
End connection | Tri-clamp | Tri-clamp | Tri-clamp | Tri-clamp
HIGH PRESSURE PUMP |  |  |  | 
MOC | SS316 | SS316 | SS316 | SS316
Quantity | 1 No | 1 No | 1 No | 1 No
MULTI PURPOSE TANK | SS316 | SS316 | SS316 | SS316
PLC | Non redundant PLC with 7" HMI |  |  | 
AKD Advanced – Fully Automatic System
TECHNICAL SPECIFICATIONS

## Slide 24
Model | AKD Basic | AKD Advanced | 
Cartridge Filter |  |  | 
MOC Housing | SS 316 | SS 316 | 
MOC Cartridge | PP Cartridge | PP Cartridge | 
Pressure Tube |  |  | 
MOC | SS 316L | SS 316L | 
High Pressure Pump |  |  | 
MOC | SS 316 | SS 316 | 
VFD | - | Available | Automatically controls the pressure of HPP
CM series Pump | Available | - | Additional pump with reduced pressure for chemical cleaning purpose
RO |  |  | 
Membrane | 4” HSRO | 4” HSRO | 
Hollow Fiber Cartridge filter | 0.05 Micron 10” SS 316 | - | 
UF | - | Polysulfone, 6000 MWCO | 
AKD Basic vs AKD Advanced

## Slide 25
Model | AKD Basic | AKD Advanced
Multi Purpose Tank with Heater |  | 
MOC | SS 316 | SS 316
UV System | Optional | Available
Valves | Manual/ Auto | Auto
Instruments |  | 
Pressure Gauge | 3 Nos | 5 Nos
Pressure Transmitter | - | 2 Nos
PH Transmitter | 1 No | 1 No
ORP analyzer | 1 No | 1 No
AKD Basic vs AKD Advanced

## Slide 26
Model | AKD Basic | AKD Advanced
Conductivity analyzer | 1 No | 2 Nos
Level Switch | 1 No | 1 No
Temperature sensor | - | 1 No
Temperature Transmitter | 2 Nos | -
Flow Indicator | 3 Nos | 1 No
Flow Transmitter | 1 No | 4 Nos
PLC | PLC with 4.3" HMI | Non redundant PLC with 7" HMI
AKD Basic vs AKD Advanced

## Slide 27
THANK YOU...